## Slide 1: Static Time Analysis(STA) for FPGA
Ahmed Abdelazeem
03/09/2022
Q-2022.3-SP2

## Slide 2: Agenda
Reg-to-Reg and I/O timing, Part1
Reg-to-Reg and I/O timing, Part2
Multiple Clocks and Exceptions
Example Project
Sequential Clocking

## Slide 3: Unit Objective
After Completing this Unit, we should be able to:
All the timing Parameters in Sequential Circuits and How to estimate Setup and Hold Constraints

## Slide 4: Synchronous Design - Reminder
The majority of digital designs are Synchronous
and constructed with Sequential Elements.
Synchronous design eliminates races (like a traffic light).
Pipelining increases throughput.
We will assume that all sequential are
Edge-Triggered, using D-Flip Flops as registers
D-Flip Flops have three critical timing parameters:
  – clock to output: essentially a propagation delay
  – setup time: the time the data needs to arrive before the clock
  – hold time: the time the data has to be stable after the clock
4

## Slide 5
Timing Parameters -
is the time from the clock edge until the data appears at the output.
The for rising and falling outputs is different.
D
Clk
Q

## Slide 6
Timing Parameters -
- Setup time is the time the data has to arrive before the clock to ensure correct sampling.
CLK
D

## Slide 7
Timing Parameters -
- Hold time is the time the data has to be stable after the clock to ensure correct sampling
CLK
D

## Slide 8
Timing Constraints
There are two main problems that can arise in synchronous logic:
  Max Delay: The data doesn’t have enough time to pass from one register to the next before the next clock edge.
  Min Delay: The data path is so short that it passes through several registers during the same clock cycle.
  Max delay violations are a result of a slow data path, including the registers’ , therefore it is often called the “Setup” path.
  Min delay violations are a result of a short data path, causing the data to change before the has passed, therefore it is often called the “Hold” path.

## Slide 9
Setup (Max) Constraints
Let’s see what makes up our clock cycle:
  After the clock rises, it takes for the data to propagate to point A.
  Then the data goes through the delay of the logic to get to point B.
  The data has to arrive at point B, before the next clock.
In general, our timing path is a race:
  Between the Data Arrival, starting with the launching clock edge.
  And the Data Capture, one clock period later.
tcq
tsetup
CLK
D
A
B

## Slide 10
Setup (Max) Constraints

## Slide 11
Hold (Min) Constraints
Hold problems occur due to the logic changing before has passed.
This is not a function of cycle time – it is relative to a single clock edge!
Let’s see how this can happen:
  The clock rises and the data at A changes after .
  The data at B changes (logic) later.
  Since the data at B had to stay stable for after the clock (for the second register), the change at B has to be at least after the clock edge.
CLK
D
A
B

## Slide 12
Hold (Min) Constraints

## Slide 13
Summary
For Setup constraints, the data has to propagate fast enough to be captured by the next clock edge:
  This set our maximum frequency.
  If we have setup failures, we can always just slow down the clock.
For Hold constraints, the data path delay has to long enough so it isn’t accidentally be the same captured:
This is independent of clock period. you can throw your chip away!

## Slide 14: Agenda
Reg-to-Reg and I/O timing, Part1
Reg-to-Reg and I/O timing, Part2
Multiple Clocks and Exceptions
Example Project
Sequential Clocking

## Slide 15: Unit Objective
After Completing this Unit, we should be able to:
Constraint all reg to reg and I/O timing paths of a single clock design for Setup timing.

## Slide 16: Unit Agenda - Part1
Constraining internal, input and output logic paths
Constraining combinational logic paths
Time-budgeting
Constraint file recommendations and constraint checking

## Slide 17: Default Design Scenario
STA Compiler assumes a "synchronously-clocked" environment.
By default:
Input Data arrives from a pos-edge clocked device.
Output Data goes to a pos-edge clocked device.

## Slide 18: Timing Analysis During/After Synthesis
STA Engine breaks design into timing paths, each with a:
Start Point
Input Port (other than a Clock Port)
Check Pin of Flipflop or Register
End Point
Output Port (other than a Clock Port)
Any Input Pin of a sequential device, except clock .
Notes: 1- "Examples of non-clock input pins of a sequential device: D (Data), S(Set) or R (Reset), E (Enable)."
Static Timing Analysis determines if a circuit meets timing constraints during and after synthesis
This involves three main steps:
1) The design is broken down into sets of timing paths
2) The delay of each path is calculated
3) Path delays are compared against
expected arrival times to determine if constraints have been met or not

## Slide 19: Constraining Register-to-Register Paths
Notes: The duty cycle matters only if your registers are clocked by both positive and negative edges of the clock. In the example down both registers are
positive-edge-triggered so the duty cycle docs not matter. The only information the user must supply is the clock period. DC retrieves the setup time of FF3 from the technology library.

## Slide 20: Constraining Register-to-Register Paths: Example
Spec:
Clock period = 2 ns
create_clock -period 2 [get_ports clk]
What is the maximum delay requirement Tmax for the register-to-register path through X in MY_DESIGN?
Answer
P – Setup = 2 – 0.2 = 1.8
Notes: "Unless explicitly defined with the -waveform option, the clock object that is created starts off going high at 0ns, comes down at 50% of the clock period, and repeats every clock period. The clock object's name is the same as the port/pin object to which it is assigned, unless explicitly defined by the -name option. The unit of time is defined in the technology library. it is commonly 1 nanosecond, as in the example above.

## Slide 21: Ideal Clock Behavior
Defining the clock in a single-clock design constrains all timing paths between registers for single-cycle, setup time
Compiler will not "buffer up" the clock network, even when connected to many clock/enable pins of flip-flops/latches
The clock network is treated as "ideal" -infinite drive capability
Zero rise/fall transition times
Zero skew
Zero insertion delay or latency
Estimated skew, latency and transition times can, and should be modeled for a more accurate representation of clock behavior

## Slide 22: Modeling Clock Trees
Compiler is NOT used to synthesize clock buffer trees
Clock tree synthesis is usually done by a physical or layout tool, based on actual cell placement.

## Slide 23: Modeling Clock Skew
Uncertainty models the maximum delay difference between the clock network branches, known as clock skew, but can also include clock jitter and margin:
set_clock_uncertainty -setup [get_clocks CLK]
Pre-Layout: Clock skew + jitter + margin
Notes: clock skew: The difference in the arrival time of a clock signal at two different registers, which can be caused by path length differences between two clock paths, or by using gated or rippled clocks. Clock skew is the most common cause of internal hold violations.

## Slide 24: Set_clock_uncertainty and Setup Time
Example:
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
Notes: By default, the command "set_clock_uncertainty" assigns the same value to the setup and the hold uncertainty, unless either the -setup or the -hold switch is used. This allows the design to be synthesized with different uncertainty numbers for setup versus hold timing, for example: For single clock timing paths, clock jitter applies to setup timing but not to hold timing, so jitter would be included in the setup uncertainty, but not in the hold uncertainty.

## Slide 25: Modeling Latency or Insertion Delay
Network latency models the average delay from create_clock port or pin to the register clock pins
Source latency models the delay from the actual clock origin to the create_clock port or pin -used for either ideal or propagated clocks (Post layout)
create_clock -period 10 [get_ports CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 3 [get_clocks CLK] ; #pre layout
# set_propageted_clock [get_clocks CLK] ; #Post layout
Notes: If you do not use the -source option with set_clock_latency, then the specified value represents network latency.
The total latency to any register (called "clock network delay"in a timing report) is equal to the source latency + network latency. In a single-clock design the launch and capture clock edges inherit the same total latency, which cancel each other out. Clock latencies are important in multi-clock designs where one clock domain with one total latency communicates with another clock domain with a different total latency.
After clock tree synthesis (CTS), clocks are no longer "ideal" - they become "propagated ".For propagated clocks, ideal network latency constraints are ignored by timing analysis and replaced by the measured latencies derived from their propagated clock buffer delays. However, source latency constraints are still added to their respective propagated network latencies to calculate the total post-CTS clock latencies."

## Slide 26: Modeling Transition Time
Transition models the rise and fall times of clock waveform at the register clock pins:
set_clock_transition -max [get_clocks CLK]

## Slide 27: Pre/Post layout Clock
create_clock -period 5 [get_ports CLK]
set_clock_latency -source -max 4 [get_clocks CLK]
set_clock_latency -max 2 [get_clocks CLK]
set_clock_uncertainty -setup 0.5 [get_clocks CLK]
set_clock_transition -max 0.08 [get_clocks CLK]
create_clock -period 5 [get_ports CLK]
set_clock_latency -source -max 4 [get_clocks CLK]
set_clock_uncertainty -setup 0.2 [get_clocks CLK]
set_propagated_clock [get_ports CLK]
synthesis (Pre-CTS) Clock Constraints
Post-CTS Clock Constraints
Notes: For post-CTS(Clock Tree Synthesis) static timing analysis set_propagated_clock forces the analyzer to calculate the ACTUAL clock tree skew, latency and transition times. The post-CTS constraints therefore do not include ideal transition and network latency commands. If the uncertainty number used during synthesis includes jitter and/or margin, these effects must still be included in the post-CTS analysis, along with the source latency.
If the network latency and clock transition constraints are kept, along with the "propagated“ clocks, these constraints are ignored during timing analysis. The actual propagated network latencies and transition times are calculated and applied. It is therefore not necessary to delete these constraints (as implied by the down post-CTS example).

## Slide 28: Constraining Input Path
Notes: ANSWER: In addition to the clock definition, the user must supply the latest arrival time of the data at input port A, with respect to FF1 's launching clock edge. In other words, an amount of time AFTER the external (Jane's) launching clock edge.
STA retrieves the setup time of FF2 from the technology library.

## Slide 29: Constraining Input Paths: Example
Spec:
Latest Data Arrival Time at Port A, after Jana's launching clock edge = 0.6
create_clock -period 2 [get_ports Clk]
set_clock_uncertainty -setup 0.3 [get_clocks Clk]
set_input_delay -max 0.6 -clock Clk [get_ports A]
MY_DESIGN .Cons
What is the maximum delay requirement Tmax for the input path N in MY_DESIGN?
Answer
P – Setup - UNC – IN_DEl = 2 – 0.2 – 0.6 – 0.3 =0.9

## Slide 30: Constraining Output Paths
Notes: ANSWER: In addition to the clock definition, the user must supply the latest arrival time of the data at output port B, with respect to FF4's capturing clock edge. In other words, the maximum "Setup" at Joe's input, with respect to Joe's Clock. This is an amount if Time Before The external capturing clock edge.

## Slide 31: Constraining Output Paths: Example
Spec:
Latest Data Arrival Time at Port B, before Joe’s capturing clock edge = 0.8
create_clock -period 2 [get_ports Clk]
set_clock_uncertainty -setup 0.3 [get_clocks Clk]
set_input_delay -max 0.6 -clock Clk [get_ports A]
set_output_delay -max 0.8 -clock Clk [get_ports B]
MY_DESIGN .Cons
What is the maximum delay requirement Tmax for the input path N in MY_DESIGN?
Answer
P - UNC – OUT_DEl = 2 – 0.3 – 0.8 – 0.3 =0.9

## Slide 32: Default I/O Clock Latency and Uncertainty
I/O clocks(set_in/output_delay -clock) inherit the same latencies and uncertainty as specified by the set_clock_latency/uncertainty commands, by default
create_clock -period 2 [get_ports Clk]
set_clock_latency -source -max 0.3 [get_clocks Clk]
set_clock_latency -max 0.12 [get_clocks Clk]
set_clock_uncertainty -setup 0.2 [get_clocks Clk]
set_input_delay -max 0.6 -clock Clk [all_inputs]
set_output_delay -max 0.8 -clock Clk [all_outputs]

## Slide 33: Multiple Inputs/Outputs -same Constraints
To constrain all inputs the same, except for the clock port:
set_input_delay -max 0.5 -clock Clk \
[remove_from_collection [all_inputs] [get_ports Clk]]
To constrain all outputs the same
set_output_delay -max 1.1 -clock Clk [all_outputs]

## Slide 34: Unit Agenda - Part 2
Constraining internal, input and output logic paths
Constraining combinational logic paths
Time-budgeting
Constraint file recommendations and constraint checking

## Slide 35: Agenda
Reg-to-Reg and I/O timing, Part1
Reg-to-Reg and I/O timing, Part2
Multiple Clocks and Exceptions
Example Project
Sequential Clocking

## Slide 36: Unit Agenda - Part 2
Constraining internal, input and output logic paths
Constraining combinational logic paths
Time-budgeting
Constraint file recommendations and constraint checking

## Slide 37: Example: Combinational Path
create_clock -period 2 [get_ports Clk]
set_clock_uncertainty -setup 0.3 [get_clocks Clk]
set_input_delay -max 0.4 -clock Clk [get_ports B]
set_output_delay -max 0.3 -clock Clk [get_ports D]

## Slide 38: Constraining a Purely Combinational Design
What is difference between this Design and The pervious one?

## Slide 39: Answer: Use a Virtual Clock!
Answer:
A clock that is not connected to any port or pin within the current design
Serves as a reference for input or output delays
Creates a clock object with a user-specified name within Compiler's memory

## Slide 40: Example: Combinational Design
create_clock -period 2 -name VClk
set_clock_uncertainty -setup 0.3 [get_clocks VClk]
set_input_delay -max 0.4 -clock Clk [get_ports A]
set_output_delay -max 0.3 -clock Clk [get_ports B]

## Slide 41: Time Budgeting (1/2)

## Slide 42: Time Budgeting (2/2)
Notes: The goal of this example is to tell the Compiler that input timing path N (including the setup time of FF2) only has 40% of the clock period. If the designer for Circuit X does also constrains their block's output path to 40% of the clock period this allows a 20% timing margin between the blocks.

## Slide 43: Time Budgeting Example

## Slide 44: Timing Constraint Summary

## Slide 45: Summary: Unit Objective
We should now be able to:
Constrain all reg_to_reg and I/O timing Paths of a single clock design for setup timing

## Slide 46: Agenda
Reg-to-Reg and I/O timing, Part1
Reg-to-Reg and I/O timing, Part2
Multiple Clocks and Exceptions
Example Project
Sequential Clocking

## Slide 47: Unit Objective
After completing this Unit, we should be able to constraint a Design with:
Multiple synchronous clocks
Clocks derived from sequential logic
Mutually exclusive synchronous clocks
Asynchronous Clocks
Multi-cycle timing

## Slide 48: Agenda – Part 1
Multiple synchronous clocks
Generated Clocks
Mutually Exclusive Synchronous Clocks
Asynchronous Clocks
Multi-Cycle Paths

## Slide 49: Multiple Synchronous Clock Designs
Multiple Clocks
All derived from the same clock source
Some clocks do not have a corresponding clock port on our design
Multiple constraints on a single port

## Slide 50: Multiple Clock Input Delay
create_clock -period 2 [get_ports CLKC]
create_clock -period 3 -name CLKB
set_input_delay -max 0.55 -clock CLKB [get_ports IN1]

## Slide 51: Maximum Internal Input Delay Calculation
To get “Common” or base period information:
report_interclock_relation
For the example shown, input logic cloud N must meet:
Notes: The following example shows the output when there are two clocks: CLKB has period of 3ns and CLKC has a period of 2ns
report_interclock_relation
***************************
Report: Interclock Relation
***************************
From period1 count1 To Period2 Count2 Common
----------------------------------------------------------------------------------------------------------------
CLKB 3.00 2 CLKC 2.00 3 6.00
CLKC 2.00 3 CLKB 3.00 2 6.00
if there is a set_false_path -from CLKC -to CLKB, then:
From period1 count1 To Period2 Count2 Common
----------------------------------------------------------------------------------------------------------------
CLKB 3.00 2 CLKC 2.00 3 6.00

## Slide 52: Maximum Internal Output Delay Calculation
create_clock -period 2 [get_ports CLKC]
create_clock -period 1 -name CLKE
create_clock -period [expr {1000/750}] -name CLKD
set_output_delay -max 0.15 -clock CLKD [get_ports OUT1]
set_output_delay -max 0.52 -clock CLKE -add_delay [get_ports OUT1]

## Slide 53: Agenda - Part 1
Multiple synchronous clocks
Generated Clocks
Mutually Exclusive Synchronous Clocks
Asynchronous Clocks
Multi-Cycle Paths

## Slide 54: Clock Propagation Through Sequential Logic
Clock definitions (create_clock) do not propagate through sequential logic

## Slide 55: Generated Clocks - Instantiated Register

## Slide 56: Agenda - Part 2
Multiple synchronous clocks
Generated Clocks
Mutually Exclusive Synchronous Clocks
Asynchronous Clocks
Multi-Cycle Paths

## Slide 57: Logically Exclusive Clocks: Problem #1
CLK1 and CLK2 are synchronous and logically mutually exclusive
create_clock -period 2.0 [get_ports CLK1]
create_clock -period [expr {1000/750}] [get_ports CLK2]
set_output_delay -max 0.15 -clock CLK1 [get_ports OUT1]
set_output_delay -max 0.52 -clock CLK1 -add [get_ports OUT1]
Notes: Answer: No! The paths through "S" and "T" may be incorrectly over-constrained because Compiler will pick the worst of the two output delay constraints and apply that to each of the paths

## Slide 58: Logically Exclusive Clocks: Solution #1
CLK1 and CLK2 are synchronous and logically mutually exclusive
create_clock -period 2.0 [get_ports CLK1]
create_clock -period [expr {1000/750}] [get_ports CLK2]
set_output_delay -max 0.15 -clock CLK1 [get_ports OUT1]
set_output_delay -max 0.52 -clock CLK1 -add [get_ports OUT1]
set_false_path -from [get_clocks CLK1] -to [get_clocks CLK2]
set_false_path -from [get_clocks CLK2] -to [get_clocks CLK1]
# OR
set_clock_groups -logically_exclusive -group CLK1 -group CLK2

## Slide 59: Logically Exclusive Clocks: Problem #2
CLK1 and CLK2 are synchronous and “Partially” mutually exclusive
create_clock -period 2.0 [get_ports CLK1]
create_clock -period [expr {1000/750}] [get_ports CLK2]
set_output_delay -max 0.15 -clock CLK1 [get_ports OUT1]
set_output_delay -max 0.52 -clock CLK1 -add [get_ports OUT1]
set_false_path -from [get_clocks CLK1] -to [get_clocks CLK2]
set_false_path -from [get_clocks CLK2] -to [get_clocks CLK1]
Notes: Answer: This will disable optimization along "legal" timing paths between CLK1 and CLK2 -paths connected by the "red" nets above.

## Slide 60: Logically Exclusive Clocks: Solution #2
CLK1 and CLK2 are synchronous and “Partially” mutually exclusive
create_clock -period 2.0 [get_ports CLK1]
create_clock -period [expr {1000/750}] [get_ports CLK2]
set_output_delay -max 0.15 -clock CLK1 [get_ports OUT1]
set_output_delay -max 0.52 -clock CLK1 -add [get_ports OUT1]
set_false_path -from [get_clocks CLK1] \
-through [get_ports OUT1] -to [get_clocks CLK2]
set_false_path -from [get_clocks CLK2] \ -through [get_ports OUT1] -to [get_clocks CLK1]

## Slide 61: Multiple Clocks Per Register : Problem #3
Multiple clocks are allowed to reach register clock pins, and are all analyzed for worst case timing
Controlled by the variable timing_enable_multiple_clocks_per_reg (true by default)
Muxed clocks are not inferred as exclusive clocks!

## Slide 62: Multiple Clocks Per Register : Solution #3

## Slide 63: Challenge Exercise
Notes: Answer: CLK1 and CLK2 are mutually exclusive for FF1 and FF2, but not for FF3 and FF4
Create generate clocks at the MUX output, and define the generated clocks as physically exclusive

## Slide 64: Challenge Exercise: Solution

## Slide 65: Agenda - Part 3
Multiple synchronous clocks
Generated Clocks
Mutually Exclusive Synchronous Clocks
Asynchronous Clocks
Multi-Cycle Paths

## Slide 66: Asynchronous Clock Designs

## Slide 67: Synthesizing with Asynchronous Clocks
It is your responsibility to design the logic in order to prevent metastability:
Instantiate double-clocking, metastable-hard Flip-Flops
Dual-port FIFO, etc.
Create Clocks to constrain the path within each clock domain
Disable timing optimization along paths between asynchronous clock domains -prevent Compiler from:
Wasting run time on a non-critical timing paths
Ignoring timing optimization of actual timing critical paths

## Slide 68: Asynchronous Designs Constraints
# Constrain register-register paths within each clock domain
create_clock -period 3 [get_ports CLKA]
create_clock -period 2 [get_ports CLKB]
# Disable timing optimization across asynchronous clock domains
set_clock_groups -asynchronous -group CLKA -group CLKB

## Slide 69: Agenda - Part 3
Multiple synchronous clocks
Generated Clocks
Mutually Exclusive Synchronous Clocks
Asynchronous Clocks
Multi-Cycle Paths

## Slide 70: Example Multi-cycle Design

## Slide 71: Timing With Multi-cycle Constraints
Where Compiler Perform Hold Analysis?
create_clock -period 2 [get_ports CLK]
set_multicycle_path -setup 6 \
-from {A_reg[*] B_reg[*]} -to C_reg[*]

## Slide 72: Default Hold Check
set_multicycle_path -setup 6 \
-from {A_reg[*] B_reg[*]} -to C_reg[*]

## Slide 73: Set the Proper Hold Constraint
set_multicycle_path -setup 6 -from {A_reg[*] B_reg[*]} -to C_reg[*]
set_multicycle_path -hold 5 -from {A_reg[*] B_reg[*]} -to C_reg[*]

## Slide 74: Summary: Unit Objective
We should now be able to Constrain a design with:
Multiple synchronous clocks
Clocks derived from sequential logic
Mutually exclusive synchronous clocks
Asynchronous Clocks
Multi-cycle timing

## Slide 75
The difference between PLL and MMCM
PLL: Phase-Locked Loop.
The frequency it generates is more prepared than DCM, and the jitter is better, but The PLL cannot dynamically adjust the phase.
MMCM: Mixed-Mode Clock Manager.
This is a PLL with a small part of DCM “Digital Clock Manager” added to it for fine phase shifting (this is the reason for its mixed mode-PLL is analog, but The phase shift is digital).
The advantage of MMCM over PLL is that the phase can be adjusted dynamically, but the area occupied by PLL is smaller.